## Slide 1: Version 3.4
Upgrades, Enhancements, and Changes
Notes: https://tslm-jira.gm.com/projects/BCIS/versions/11105

## Slide 2: Major Changes

## Slide 3: Allow For Dual VRFM
The original BEV3 packs had a VRFM in them
The ET1B packs have a dual VRFM in them
The iTest code to interface with the VRFM was updated to support this new mode of operation

## Slide 4: Allow For More Cells
iTest has always been configured for 120 cells in a pack
ET1B has more than 120 cells so wasn’t going to work with the current architecture
We migrated from manually created channels to array channels
The solution now support up to 200 channels
Name changes:
  Old - vBLINC1Cell_[000-001]
  New - varBLINC1Cells_0[0-100]
  New - varBLINC1Cells_1[0-100]

## Slide 5: Make All Faults Call Out
During normal business hours the stand owner will be notified of a fault directly from PD
Faults will not post to Slack
Anytime a red fault box appears on a test stand, there will be a PD notification that will go out as well
Stand Owner Quick Start
On-call Quick Start

## Slide 6: Misc Improvements
Skip the charge step at the beginning of HPPC during NPt
Fix shaker not reporting nominal status
Make more python scripts compatible with python version 3
Improve pagerduty support for China
Simplify and improve the calibration module
Add additional logging for the BSS